## Slide 1
Predictive Maintenance for Turbofan Engines
From Reactive Repairs to Real-Time Remaining Useful Life Forecasting
NASA C-MAPSS FD001 · Random Forest RUL Estimator
Samson Mayomi Matthew

## Slide 2
The Cost of Not Knowing When an Engine Will Fail
REACTIVE
Fix it after it breaks.
Risk: catastrophic in-flight failure
SCHEDULED
Service on a fixed calendar.
Cost: wasted usable engine life
PREDICTIVE
Service when the data says to.
Requires: a reliable RUL estimate
The missing input across all three models: a reliable, data-driven RUL estimate
TURBOFAN RUL · NASA C-MAPSS FD001
02

## Slide 3
Objective: A Data-Driven RUL Estimator
Estimate Remaining Useful Life — in cycles — for a turbofan engine at any point in its operating history, using only its own sensor telemetry.
Input: sensor telemetry at cycle t → Output: predicted cycles to failure
SCOPE OF THIS PROOF OF CONCEPT
Dataset
FD001
Conditions
Sea-level, single regime
Operating Mode
One operating condition
Fault Mode
Single dominant fault path
TURBOFAN RUL · NASA C-MAPSS FD001
03

## Slide 4
NASA C-MAPSS FD001: Multivariate Run-to-Failure Telemetry
100
Training Engines
20,631 records · run-to-failure
100
Test Engines
13,096 records · truncated
24
Raw Input Channels
21 sensors + 3 operating settings
unit | time_cycles | op_set_1 | op_set_2 | op_set_3 | sensor_1 | sensor_2 | … | sensor_21
1 | 1 | -0.0007 | -0.0004 | 100.0 | 518.67 | 641.82 | … | 23.4190
1 | 2 | 0.0019 | -0.0003 | 100.0 | 518.67 | 642.15 | … | 23.4236
Train = full run-to-failure history through final cycle Test = truncated before failure, true RUL supplied via ground-truth vector
TURBOFAN RUL · NASA C-MAPSS FD001
04

## Slide 5
Step One: Removing Signals That Carry No Information
24 → 16
Modeling features remaining after variance screening
2 operating settings + 14 live sensors
op_setting_3
σ = 0
sensor_1
σ = 0
sensor_5
σ = 0
sensor_6
σ = 0
sensor_10
σ = 0
sensor_16
σ = 0
sensor_18
σ = 0
sensor_19
σ = 0
Zero variance = zero discriminative power — removed before model training
TURBOFAN RUL · NASA C-MAPSS FD001
05

## Slide 6
Building the Label: Run-to-Failure vs. Truncated Ground Truth
TRAINING SET
RUL = max_cycle − current_cycle
Exact — engine runs to actual failure
TEST SET
RUL = ground_truth + (max_cycle − current_cycle)
Anchored — trajectory truncated before failure
Training target capped at 125 cycles (piecewise RUL) — prevents overfitting to flat, pre-degradation regions
Chart: Illustrative target shape — raw vs. piecewise-capped RUL
| 0 | 25 | 50 | 75 | 100 | 125 | 150 | 175 | 200
Raw RUL (uncapped) | 280 | 245 | 210 | 175 | 140 | 105 | 70 | 35 | 0
Piecewise-Capped RUL | 125 | 125 | 125 | 125 | 125 | 105 | 70 | 35 | 0
TURBOFAN RUL · NASA C-MAPSS FD001
06

## Slide 7
Why We Split by Engine, Not by Row
■ 80 Train Engines ■ 20 Validation Engines
16,340
Training Rows
4,291
Validation Rows
0
Overlapping Engines
StandardScaler fit on the training partition only — no leakage into validation
TURBOFAN RUL · NASA C-MAPSS FD001
07

## Slide 8
Two Architectures, One Question: Distance or Ensemble?
K-Nearest Neighbors
Distance-Based Baseline
Predicts via closest points in feature space
Sensitive to local sensor noise in 16-dim space
No structural assumption about degradation shape
Random Forest Regressor
Bagging Ensemble — Selected Architecture
150 trees, max depth 12
Averages across decorrelated decision trees
Smooths sensor jitter, captures non-linear interactions
TURBOFAN RUL · NASA C-MAPSS FD001
08

## Slide 9
Why RMSE Is the Metric That Matters Here
19.60
RMSE (cycles)
13.96
MAE (cycles)
0.777
R²
Random Forest — held-out validation engines
K-Nearest Neighbors
Degrades under sensor noise — local distance metric pulled off-course by spikes in high-dimensional readings.
Random Forest
Stable under noise — ensemble averaging across decorrelated trees smooths fluctuations and dampens spikes.
RMSE is prioritized over MAE: large errors carry outsized operational risk in turbine degradation
TURBOFAN RUL · NASA C-MAPSS FD001
09

## Slide 10
Opening the Black Box: Gini Importance Mapped to Physics
Gini importance extracted directly from the trained forest
Weights mapped back to physical subsystems, not treated as abstract scores
Top features align with thermal and rotational stress — not noise
Exact importance values were rendered as a plot in the source notebook; relative ranking is shown here.
Thermal stress — exhaust gas temperature
Rotational dynamics — HP compressor speed
Remaining 14 monitored sensors (lower relative weight)
TURBOFAN RUL · NASA C-MAPSS FD001
10

## Slide 11
Engines Don't Degrade Gradually — They Accelerate
Chart: Illustrative degradation pattern — Engine Unit #5
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Stress-indicator sensor trend | 2 | 3 | 3 | 4 | 5 | 8 | 16 | 28 | 44 | 63 | 85
~Cycle 90
Early life: stable baseline → Late life: compounding degradation
TURBOFAN RUL · NASA C-MAPSS FD001
11

## Slide 12
Turning RUL Output Into a Maintenance Work Order
GREEN — RUL > 50 cycles
Normal operations. Maintain baseline telemetry monitoring.
YELLOW — RUL 21–50 cycles
Flag asset for inspection at next stopover. Pre-order wear components.
RED — RUL ≤ 20 cycles
Immediate grounding. Avoid in-flight shutdown or core structural failure.
TURBOFAN RUL · NASA C-MAPSS FD001
12

## Slide 13
Scaling the Architecture: What's Next
NOW
FD001 Baseline
Single operating condition. End-to-end pipeline validated on held-out engines.
NEXT
Formalize Piecewise Cap
Rigorously test 125 vs. 130-cycle RUL caps rather than a single fixed assumption.
LATER
Multi-Regime Scaling
Extend to FD002 / FD004 — altitude, ambient temperature, and payload variation.
TURBOFAN RUL · NASA C-MAPSS FD001
13

## Slide 14
We turned raw, noisy sensor telemetry into a Remaining Useful Life estimate accurate to within roughly 20 cycles — and one we can explain.
Accurate
RMSE 19.6 cycles on held-out engines
Interpretable
Importances trace to known failure physics
Actionable
Maps directly to a tiered maintenance protocol
Questions & Discussion
TURBOFAN RUL · NASA C-MAPSS FD001
14